## Slide 1: Logan City municipal water modeling
Prepared by: Muhammad Imran
Nour Atallah
Instructor: Dr. David Rosenberg
CEE-6490 River Basin Planning
04-28-2016

## Slide 2: Outline
Problem Statement
Objective
Background
Forecasting
Performance Metrics
Alternatives and Alternative Evaluation
Conclusion

## Slide 3: Problem Statement
The city of Logan is facing a increase level of population growth, which will result in failure of system to meet future demand in 2050.
Stakeholder
City of Logan

## Slide 4: Background
Logan is a county seat in Cache County, Utah
Water rights for municipal use in Logan are 79 cfs
Water supply capacity is 69 cfs mainly through DeWitt Springs
Logan City Public Works Department

## Slide 5: Objectives
Make recommendations for structural and non-structural improvements to current water supply systems.
Examine how the proposed system will improve the current situation using WEAP.

## Slide 6: Demand Calculation for Logan
Annual total demand = 12,000 ac-ft
Monthly demand in Winter season = 3.2% of total demand
      384 ac-ft
      Multiplied by 5 to winter demand
Monthly demand in Summer season = 12% of total demand
      1,440 ac-ft
      Multiplied by 7 to get summer demand

## Slide 7: Performance Metrics
Reliability, Resiliency and Vulnerability (RRV)
  Water supply system performance indicator
Unmet Demand (AF)
  Systems inability to meet the municipal demand

## Slide 8: Management Alternatives
Non - Structural Measure
  Reduce the per capita water demand by 25%
  Structural Measure
  Build and operate the Above Cutler Reservoir

## Slide 9: Scenarios for WEAP Modelling
Reference Scenario
Scenario with water conservation
Scenario with Above Cutler reservoir
Scenario with water conservation and Above Cutler reservoir

## Slide 10: WEAP Model

## Slide 11: Alternatives Evaluation (WEAP Outputs)
Scenario/Indicator | Reliability (%) | Resiliency (%) | Vulnerability (AF)
Reference | 82.72 | 22.35 | 1,393.59
Reduced Demand | 82.72 | 22.35 | 1,071.46
Above Cutler | 87.6 | 23.23 | 1,360.78
Above Cutler and Reduced Demand | 88.01 | 27.12 | 1,064.32

## Slide 12: Evaluation Relative to Reference
Scenario/Indicator | Reliability (%) | Resiliency (%) | Vulnerability (%)
Reduced Demand | 00.00 | 00.00 | 23.12
Above Cutler | 5.9 | 17.34 | 2.35
Above Cutler and Reduced Demand | 6.39 | 21.32 | 23.63

## Slide 13: Alternative Evaluation
Chart: Reliability and Resiliency Evaluation
| Reference | Reduced Demand | Above Cutler | Reduced Demand & Above Cutler
Reliability (%) | 82.72 | 82.72 | 87.6 | 88.01
Resiliency (%) | 22.35 | 22.35 | 23.23 | 27.12

## Slide 14: Alternative Evaluation
Chart: Vulnerability Evaluation
| Reference | Reduced Demand | Above Cutler Reservoir | Reduced Demand & Above Cutler
Vulnerability | 1393.59 | 1071.46 | 1360.78 | 1064.32

## Slide 15: Alternative Evaluation (Unmet Demand)
 | Oct. | Nov. | Dec. | Jan. | Feb. | Mar. | Apr. | May. | June. | Jul. | Aug. | Sep.
Reference | 451 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 35 | 315 | 578 | 724 | 786
Reduced Demand | 338 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 26 | 245 | 457 | 562 | 593
Above Cutler | 451 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 108 | 306 | 443 | 716
Combined | 338 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 87 | 233 | 334 | 539
Units in AF

## Slide 16: WEAP Outputs (Bear River Canal Company)
Scenario/Indicator | Reliability (%) | Resiliency (%) | Vulnerability (AF)
Reference | 85 | 100 | 9,871
Reduced Demand | 85 | 100 | 9,959
Above Cutler | 90 | 100 | 8,351
Combined | 90 | 100 | 8,351

## Slide 17: WEAP Outputs (Bear River Migratory Bird Refugee)
Scenario/Indicator | Reliability (%) | Resiliency (%) | Vulnerability (AF) | Monthly Bird Use (%)
Reference | 84 | 30 | 25,326 | 88.29
Reduced Demand | 85 | 30 | 25,359 | 88.43
Above Cutler | 89 | 35 | 23,682 | 93
Combined | 90 | 35 | 23,836 | 93

## Slide 18: WEAP Outputs (Pacific Corp)
Scenario/Indicator | Annual Avg. Unmet Demand Relative to Reference (%) | Annual Avg. Power Generated Relative to Reference (MW)
Reduced Demand | -6% | 4
Above Cutler | +161.5% | 47
Combined | +170% | 48
+: Excess
- : Deficit

## Slide 19: Overall Evaluation
Stakeholder/Indicator | Reliability (%) |  |  | Resiliency (%) |  |  | Vulnerability (AF) |  | 
Scenario | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3
Logan | 87.72 | 87.6 | 88 | 22.35 | 23.23 | 27.12 | 1,071.5 | 1,360.8 | 1,064
BRCC | 85 | 90 | 90 | 100 | 100 | 100 | 9,959 | 8,351 | 8,351
BRMBR | 85 | 89 | 90 | 30 | 35 | 35 | 25,359 | 23,682 | 23,836
Avg. | 86 | 89 | 89 | 51 | 52 | 54 | 12,130 | 11,131 | 11,084
1 : Reduced Demand Scenario
2 : Above Cutler Reservoir Scenario
3 : Combined Scenario

## Slide 20: Conclusion and Recommendations
Reduce Demand: it was obvious that reducing the residential water use by (25%) did not make that significant improvements on the system performance metrics relative to the base case.
Above Cutler Reservoir: Building and operating the reservoir will be a very good option if considered.
Reduce Demand & Above Cutler Reservoir: Even this system improved the performance criteria, the system did not show that significant improvement comparing to Above Cutler Reservoir scenario.

## Slide 21
Questions ?

## Slide 22: References
J. R. Lund (2008). “Approaches to Planning Water Resources”
Logan Public Works Department (2015), “Logan Water Conservation Plan”
  www.loganutah.org/document_center/.../Water%20Conservation.pdf
  Utah Division of Water Rights (2016), “Public Water Supplier Information
  http://www.waterrights.utah.gov/cgi-bin/wuseview.exe?Modinfo=Pwsview&SYSTEM_ID=1112
  Wikipedia webpage, “Logan, Utah” - https://en.wikipedia.org/wiki/Logan,_Utah